## Slide 1
RASPBERRY PI WORKSHOP

## Slide 2: OUTLINE
SETUP
REMOTE ACCESS
LINUX COMMANDS
PYTHON PROGRAMMING
  LEDs
  TEMPERATURE
  GUI

## Slide 3: SETUP

## Slide 4: GETTING STARTED
Download Raspbian and Extract Zip Files
  https://www.raspberrypi.org/downloads/

## Slide 5: GETTING STARTED
Install win32DiskImager
  https://sourceforge.net/projects/win32diskimager

## Slide 6: GETTING STARTED
Format SD Card
  Panasonic SD Formatter

## Slide 7: GETTING STARTED
Write image to SD Card
  Using win32DiskImager
Click WRITE

## Slide 8: GETTING STARTED
Insert SD Card on Raspberry Pi
Access via Direct Setup or Headless Setup
Wait
Finished 

## Slide 9: REMOTE ACCESS

## Slide 10: REMOTE CONNECTION
SSH (Secure Shell)
VNC or REMOTE DESKTOP
ACCESS OVER INTERNET
SFTP (Secure File Transfer Protocol)

## Slide 11: SSH (Secure Shell)
Connect RPi to laptop via Ethernet cable
Use Advanced IP Scanner software to scan IP Address of RPi
  https://www.advanced-ip-scanner.com/

## Slide 12: SSH (Secure Shell)
Input IP Address to Putty.

## Slide 13: SSH (Secure Shell)
Default:
  Login as: pi
  Password: raspberry
Click Enter

## Slide 14: SSH (Secure Shell)
Terminal

## Slide 15: VNC or Remote desktop
After connecting to Terminal via Putty (SSH)
Enter to Terminal:
  sudo apt-get install xrdp (remote desktop)
  sudo apt-get install realvnc-vnc-viewer (VNC – Virtual Network Computing)

## Slide 16: VNC or Remote desktop
Run the command:
  sudo raspi-config, navigate to: Advanced Options > VNC > select Yes
  By default, VNC Server remotes the graphical desktop running on your Raspberry Pi.

## Slide 17: VNC
FOR VNC
  IP ADDRESS OF Rpi is required

## Slide 19: Remote desktop
FOR REMOTE DESKTOP
  IP ADDRESS OF Rpi is required
  Login as: pi
  Password: raspberry

## Slide 20: Remote desktop
Username: pi
Password: raspberry

## Slide 21: VNC or Remote desktop
Username: pi
Password: raspberry

## Slide 23: ACCESS OVER INTERNET
On laptop: got to Apps & Features
Manage Optional Features
Install OpenSSH Client (Beta)
Install OpenSSH Server (Beta)

## Slide 24: ACCESS OVER INTERNET
On Terminal:
Run ifconfig

## Slide 25: ACCESS OVER INTERNET
On Terminal:
Use the IP Address to Putty or VNC or Remote Desktop
Remove Ethernet Cable

## Slide 26: SFTP
SSH File Transfer Protocol
  Extension of the SSH to handle file transfers
  Programs
    FileZilla, WinSCP

## Slide 27: SFTP - Filezilla

## Slide 28: ACTIVITY

## Slide 29: ACTIVITY (SFTP)
On your Desktop:
  Create a file.txt and rename the file.
  Download the mp4 file to your Desktop
  Transfer the 2 files to your Rpi Desktop

## Slide 30: Linux commands

## Slide 31: GENERAL COMMANDS
clear
  Clears previously run commands and text from the terminal screen.
Date
  Prints the current date.
find / -name example.txt
  Searches the whole system for the file example.txt and outputs a list of all directories that contain the file.
nano example.txt
  Opens the file example.txt in the Linux text editor Nano.

## Slide 32: GENERAL COMMANDS
sudo raspi-config
  Opens the configuration settings menu.

## Slide 33: FILE AND DIRECTORY COMMANDS
cat example.txt
  Displays the contents of the file example.txt.
cd /abc/xyz
  Changes the current directory to the /abc/xyz directory.
cp XXX:
  Copies the file or directory XXX
mv XXX
  Moves the file or directory named XXX to a specified location.
Notes:   CP
  and pastes it to a specified location; i.e. cp examplefile.txt /home/pi/office/ copies examplefile.txt in the current directory and pastes it into the /home/pi/ directory. If the file is not in the current directory, add the path of the file’s location (i.e. cp /home/pi/documents/examplefile.txt /home/pi/office/ copies the file from the documents directory to the office directory).
MV
  For example, mv examplefile.txt /home/pi/office/ moves examplefile.txt in the current directory to the /home/pi/office directory. If the file is not in the current directory, add the path of the file’s location (i.e. cp /home/pi/documents/examplefile.txt /home/pi/office/ moves the file from the documents directory to the office directory). This command can also be used to rename files (but only within the same directory). For example, mv examplefile.txt newfile.txtrenames examplefile.txt to newfile.txt, and keeps it in the same directory.

## Slide 34: FILE AND DIRECTORY COMMANDS
rm example.txt
  Deletes the file example.txt.
rmdir example_directory
  Deletes the directory example_directory (only if it is empty).
scp user@10.0.0.32:/some/path/file.txt
  Copies a file over SSH..
touch example.txt
  Creates a new, empty file named example.txt in the current directory.
Notes: SCP
  Can be used to download a file from a PC to the Raspberry Pi. user@10.0.0.32 is the username and local IP address of the PC, and /some/path/file.txt is the path and file name of the file on the PC.

## Slide 35: NETWORKING AND INTERNET COMMANDS
ifconfig
  To check the status of the wireless connection you are using (to see if wlan0 has acquired an IP address).
iwconfig
  To check which network the wireless adapter is using.
iwlist wlan0 scan
  Prints a list of the currently available wireless networks.

## Slide 36: NETWORKING AND INTERNET COMMANDS
nmap
  Scans your network and lists connected devices, port number, protocol, state (open or closed) operating system, MAC addresses, and other information.
ping
  Tests connectivity between two devices connected on a network. For example, ping 10.0.0.32 will send a packet to the device at IP 10.0.0.32 and wait for a response. It also works with website addresses.
wget http://www.website.com/example.txt
  Downloads the file example.txt from the web and saves it to the current directory.

## Slide 37: SYSTEM INFORMATION COMMANDS
cat /proc/meminfo
  Shows details about your memory.
cat /proc/partitions
  Shows the size and number of partitions on your SD card or hard drive.
cat /proc/version
  Shows you which version of the Raspberry Pi you are using.
df –h
  Shows information about the available disk space.

## Slide 38: SYSTEM INFORMATION COMMANDS
df /
  Shows how much free disk space is available.
dpkg – –get–selections
  Shows all of your installed packages.
free
  Shows how much free memory is available.
hostname –I
  Shows the IP address of your Raspberry Pi.
lsusb
  Lists USB hardware connected to your Raspberry Pi.

## Slide 39: SYSTEM INFORMATION COMMANDS
PRESS UP KEY
  print the last command entered into the command prompt. This is a quick way to repeat previous commands or make corrections to commands.
vcgencmd measure_temp
  Shows the temperature of the CPU.
vcgencmd get_mem arm && vcgencmd get_mem gpu
  Shows the memory split between the CPU and GPU.

## Slide 40: Linux Commands
SHUTDOWN
sudo halt
REBOOT
sudo reboot

## Slide 41: NEVER RUN THIS COMMAND
rm –rf/

## Slide 42: Updating raspian os
sudo apt-get update
Synchronizes the list of packages on your system to the list in the repositories. Use it before installing new packages to make sure you are installing the latest version.sudo
sudo apt-get upgrade
Upgrades all of the software packages you have installed.

## Slide 43: PyTHON PROGRAMMING

## Slide 44: LEDs

## Slide 45: BLINKING AN LED THROUGH GPIO PINS

## Slide 46: Objectives
Familiarization to Rpi’s GPIO Pins
Turning ON the LED
Blinking an LED

## Slide 47: Familiarization to Rpi’s GPIO Pins

## Slide 48: Turning ON the LED – Testing

## Slide 49: Turning ON the LED – Hardware

## Slide 50: Turning ON the LED – Software

## Slide 51: Blinking an LED

## Slide 52: Raspberry pi Web server

## Slide 53: Web server
A program that uses HTTP to serve the files that form Web Pages to users
In Python, the Flask web-framework is used as a web server
The Flask library is built-in
The Flask library is used to access the GPIO PINS via Web Server

## Slide 54: HARDWARE

## Slide 55: steps
sudo python app.py
Determine the IP Address of your Raspberry Pi
Open a web browser (pc, phone, tablet)
Input the IP Address into the web browser
Toggle the ON/OFF Button

## Slide 56: Input the IP Address into the web browser

## Slide 57: Toggle the ON/OFF Button

## Slide 58: CAYENNE

## Slide 59: Cayenne
An IoT-based online application platform
  Raspberry Pi
  Arduino
Drag and Drop
Customizable
Wide range of available sensors
Available in Play Store and Apple Store

## Slide 60: Cayenne Interface (Desktop)

## Slide 61: Cayenne Interface (Smartphone)

## Slide 62: Cayenne Interface (GPIO)

## Slide 63: LED Sample

## Slide 64: Steps
Install Cayenne on your Android or iPhone
Connect your phone to your Raspberry Pi.
Create account
Add New >>
Device/Widget
Actuators >> Light
Channel 18
Choose Icon >> Light
Add Actuator

## Slide 65: Temperature SENSOR

## Slide 66: Interfacing Temperature Sensor with Raspberry Pi

## Slide 67: Objectives
Setting up the DS18B20 – Digital Temperature Sensor
Temperature monitoring through Python IDLE & CLI.

## Slide 68: DS18B20 – Digital Temperature Sensor
DATA
GND
VCC

## Slide 69: How to connect Temperature Sensor to Raspberry Pi?

## Slide 70: Raspberry Pi – Set Up
Add 1-Wire Support
Add module from the Linux Kernel (w1-gpio, and w1-them)
Read the contents of the digital temperature sensor
Install w1thermsensor Python module

## Slide 71: Add 1-Wire Support
>>sudo nano /boot/config.txt
Add the following: dtoverlay=w1-gpio
Reboot the RPi

## Slide 73: Add module from the Linux Kernel
>>sudo modprobe w1-gpio
>>sudo modprobe w1-therm

## Slide 75: Read the contents of the digital temperature sensor
>>cd /sys/bus/w1/devices
>>ls
>>cd 28-nnnnnn
>> cat w1_slave

## Slide 76
Current Temperature Reading

## Slide 77: Install w1thermsensor Python module

## Slide 78: Temperature Monitoring through CLI

## Slide 79: Temperature monitoring through Python IDLE

## Slide 80: GRAPHICAL USER INTERFACE

## Slide 81: TK-INTER PYTHON GUI PROGRAMMING

## Slide 82: Objectives
Introduce Tkinter – a python GUI module
Create an empty window using Tkinter
Customizing your window
Adding widgets to your window
Customizing the added widgets
Button – Callback Functions
Display sensor data through GUI

## Slide 83: Introduce Tkinter – a python GUI module
It is the standard GUI Module for Python. It provides a power object-oriented interface to the TK GUI toolkit
Supported widgets of Tkinter

## Slide 84: Create an empty window using Tkinter
Empty Window

## Slide 85: Customizing your window
Changing window title
Changing window size
Changing window color

## Slide 86: To change window title

## Slide 87: To change window size

## Slide 88: To change window color

## Slide 89: Adding widgets to your window
Syntax used to add widgets:
my_widget = Widget-name(its container, ** its configuration options)
Widgets we will be using

## Slide 90: Adding widgets to your window

## Slide 91: Customizing the added Widgets

## Slide 92: Button – Callback Functions
A callback function is a function that is executed when the user pressed a button

## Slide 94: Display sensor data through GUI

## Slide 97: EXERCISES

## Slide 98: Exercises
Create a program that will automatically email iecep.raspberry@gmail.com when the temperature reach a certain set point.
Create a program that will turn ON the LED whenever the user push button 1, and will turn OFF the LED when button 2 is pressed.

## Slide 99: Exercise (CAYENNE)
Connect your digital temperature sensor
  Determine your 1-Wire Address
  Channel 4